The PFR-100 series, a small and high-performance programmable D.C. power supply, adopts natural convection design to dissipate heat. The fanless structure allows users to focus on their experiments and tests in a quiet environment. Fanless power supply will not suck in dust and foreign objects, therefore, PFR-100 has a longer life cycle compared with that of power supplies with fan.

The PFR-100 series is a power supply with a five-fold rated power that allows users to self-define voltage and current under rated power conditions so as to satisfy them with wider voltage and current operational ranges. PFR-100, with rated 100W, provides two models: PFR-100L- maximum output voltage of 50V (at 2A) or maximum output current of 10A (at 10V); PFR-100M- maximum output voltage of 250V (at 0.4A) or maximum output current of 2A (at 50V).

The PFR-100 series provides front and rear panel output terminals. The front panel output terminal helps users shorten test lead replacement time while conducting adjustment on front panel’s function keys. The rear panel output terminal facilitates an easy wiring operation for rackmount assembly. 3U height, 70mm width and 2.5KG in weight have greatly elevated PFR-100’s portability. Furthermore, the multi-drop mode allows users to control up to 31 PFR-100s without using switch/Hub that help users save the equipment cost.

The LAN interface for PFR-100 is Ethernet port. PFR-100 also has a built-in web server and intuitive user interface. Users, via general browsers including Internet Explorer, Mozilla Firefox or Android cellular phones, can monitor FRP’s test and measurement anywhere. Users not only can remotely monitor PFR-100 via internet, but also remotely observe and adjust their operating PRF-100s in the lab from your home. The outputs of PFR-100 can be monitored including OVP, OCP, UVL; and the system information can be checked such as unit’s serial number, firmware edition and internet setting. Users can remotely adjust PFR-100 settings, including output voltage/current, the slew rate for voltage/current, Bleeder circuit control, OCP, delayed time for output voltage and Buzzer settings.

The PFR-100 series provides special functionalities to meet test requirements for different load’s characteristics. The CC priority mode can be applied for DUTs with diode characteristics to prevent DUT from being damaged by inrush current. A slow rise time for voltage can also protect DUT from inrush current, especially for tests on capacitive load. When power is off or load is disconnected, the activation of Bleeder circuit control will allow the bleeder resistor to consume filter capacitor’s electricity. Without the bleed resistor, power supply’s filter capacitor may still have electricity that is a potential hazard. For automatic testing equipment systems, the bleeder resistor allows PFR-100 to rapidly discharge to prepare itself for the next operation.

Features

| Five-fold rated power output Natural convection cooling design (fanless structure) Three-point memory storage function Output ON/OFF delayed time function CV, CC priority mode Adjustable slew rate for voltage/current Bleeder circuit control | Protections: OVP, OCP, AC FAIL and OTP Support front and rear panel output Built-in USB and RS-232/485 interfaces. Options: LAN and GPIB Remotely monitor and control via internet (PFR-100 has a built-in web server.) External analog control and monitor function Remote compensation and detection for voltage function |
| --- | --- |

| Customers and Applications |
| --- |
| Customers LED industrial applications Rechargeable battery/capacitor Semi-conductor industry Motor Solar power industry | Applications LED module test and reliability test Charging test for a single battery DC/DC converter applications DC motor test applications Solar module quality test |

Outlook

| Front panel | Rear panel |
| --- | --- |
| Voltage knob Current knob Output button USB A port Output terminal Power switch [ON]/[OFF] Display area | External analog remote control connector Output terminals Line voltage input GPIB (factory installed option) Remote In (RS-232 or RS-485) | Remote Out (RJ-45) LAN (factory installed option) USB |

Important Information of Product Ordering

Key Dates for Product Announcement

- NPI (Dec 21, 2017)

- Order Queue Open (Dec 29, 2017)

- Global Market Announcement (Jan 29, 2018)

Service Policy

- PFR-100 fanless multi-range DC power supply carries one year warranty.

- Contact GW Instek Service Department for maintenance information.

Ordering Information

- PFR-100L(0~50V/ 0~10A / 100W) Fanless Multi-Range DC Power Supply

- PFR-100M(0~250V/ 0~2A / 100W) Fanless Multi-Range DC Power Supply

Standard Accessories

CD (User Manual, Programming manual) x 1, Power cord x 1

GTL-134 test lead x 1

Accessory packages:

GTL-104A test lead & PFR-001 accessory kit (for PFR-100L only)

GTL-105A test lead & PFR-002 accessory kit (for PFR-100M only)

Option (factory installed)

| PFR-GL | LAN + GPIB interface |
| --- | --- |

Optional Accessories

| GTL-258 PSU-232 PSU-485 GTL-246 | GPIB Cable, 2000mm RS-232 Cable with DB9 Connector Kit. RS-485 Cable with DB9 Connector Kit USB Cable (USB 2.0 Type A- Type B Cable, |
| --- | --- |
| GRA-431-J-100 GRA-431-J-200 GRA-431-E-100 GRA-431-E-200 | Rack mount adapter (JIS) with AC 100V Rack mount adapter (JIS) with AC 200V Rack mount adapter (EIA) with AC 100V Rack mount adapter (EIA) with AC 200V |

Detailed Product Information

Detailed Descriptions for Features	3

Operating range	3

C.V/C.C priority mode	3

Adjustable Slew Rate	3

Web server remote control function	3

Bleeder Circuit Control	3

Remote program control (Up to 31 units connection)	3

External analog control function	3

Comparison	3

Features, Advantages and Benefits	3

Features Comparison	3

SPECIFICATION	3

Output	3

Constant Voltage Mode	3

Constant Current Mode	3

Protection Function	3

Analog Programming and Monitoring	3

Front Panel	3

Programming and Measurement (RS-232/485, USB, LAN, GPIB)	3

Input Characteristics	3

Interface Capabilities	3

Environment Conditions	3

Detailed Descriptions for Features

| Operating range |
| --- |
|  | Output voltage, output current and rated power of PFR-100 are as follows: Model PFR-100L Output channel 1 Output voltage 0 – 50V Output current 0~ 10A Rated power 100W Model PFR-100M Output channel 1 Output voltage 0 – 250V Output current 0~ 2A Rated power 100W |

| C.V/C.C priority mode |
| --- |
| Under the conventional C.V mode, inrush current and surge voltage appeared at forward voltage (Vf) of LED Under C.C priority mode, inrush and surge voltage are effectively restrained. | Under the application conditions of diode load, conventional power supplies under the CV priority mode will produce inrush current and surge voltage at turn-on. The PFR-100 series has CV and CC priority modes. The CC priority mode can prevent inrush current and surge voltage from occurring at turn-on to protect DUT |
| Adjustable Slew Rate |
| Adjustable voltage slew rate Adjustable current slew rate | The PFR-100 series can adjust slew rate for current and voltage. Via setting the rise and fall time of voltage and current, users can verify DUT’s characteristics during voltage and current variation. Additionally, slew rate adjustment can mitigate voltage shift to effectively prevent DUT from being damaged by inrush current. This function is ideal for tests such as capacitive load and motor. |
| Voltage Slew Rate | Current Slew Rate |
| 0.1V~100.0V/sec (PFR-100L) 0.1V~500.0V/sec (PFR-100M) | 0.01A~20.00A / sec (PFR-100L) 0.001A~4.000A / sec (PFR-100M) |

| Web server remote control function |
| --- |
|  | Users, via general browsers including Internet Explorer, Mozilla Firefox or Android cellular phones, can monitor FRPs’ test and measurement anywhere. Users not only can remotely monitor PFR-100 via internet, but also remotely observe and adjust your operating PRF-100 in the lab from your home. The outputs of PFR-100 can be monitored including OVP, OCP, UVL; and system information can be checked such as unit’s serial number, firmware edition and internet setting. Users can remotely adjust PFR-100 settings, including output voltage/current, the slew rate for voltage/current, Bleed circuit control, OCP, delayed time for output voltage and Buzzer settings. |

| Bleeder Circuit Control |
| --- |
| PFR-100 Series Bleeder Circuit | The PFR-100 series power supply has a bleeder circuit control which is in parallel with the output terminal. When power is off or load is disconnected, the bleed resistor will consume electricity from the filter capacitor. Without a bleed resistor, the filter capacitor of power could still be charged with electricity that poses a potential danger. In addition, for ATE system, bleed resistor allows the PFR-100 series to bleed current rapidly so as to prepare itself for the next operation. |

| Remote program control (Up to 31 units connection) |
| --- |
|  | Provide USB, GPIB and LAN for PC to remote control Master PFR-100. RJ-45 connector on the rear panel can connect up to 31 units. LAN or USB remote control and augmenting slave units by using the multi-drop mode will no longer need any switch/hub that can help customers save equipment costs. |
| External analog control function |
| External voltage controls voltage range | The rear panel of the PFR-100 series has an analog control terminal. The external analog control interface allows external voltage or resistance to control voltage and current output; and allows power supply to output or to be turned on and off. The diagram on the left shows typical connection methods for external control applications. For more detailed connection information please refer to user manual. |
| External resistance controls voltage range |  |
| External on-off to control output, on or off |  |

Comparison

## Features, Advantages and Benefits

| Feature | Advantages | Benefits |
| --- | --- | --- |
| Five-fold rated power multi-range operation | Under a fixed power, larger voltage and current outputs can be covered. | For DUT with different voltage ranges, users don’t have to additionally procure power supply with different voltage ranges. |
| Natural convection cooling design (fanless structure) | While in operation, PFR-100 is very quiet and will not suck in dust. | It is ideal for DUT with noise test requirement and tests in poor environment. |
| Web server remote control function (optional LAN interface is required) | Users, via browsers, can conduct monitoring and control. | Via internet connection, users don’t have to sit in front of instrument to operate it. |
| Support multiple interfaces | Standard interfaces: USB, RS-232/ RS-485 Options：LAN & GPIB (factory installed) | Users can select suitable interfaces to conduct connection operation and automatic control. |
| Adjustable Slew rate | Determine the rise/fall time for voltage and current based upon applications. | It is beneficial for users in conducting detailed analysis and characteristic test on DUT. |
| An elaborate 3U height and 70mm width dimension | Highly portable and a space saver | By user’s requirements, it can be integrated into a system or be rack mounted. |
| External analog remote control terminal | Simple voltage, resistance and on/off circuit can monitor. | It satisfies analog control power supply users such as PLC control. |

## Features Comparison

| Items | GW Instek/TTC | Takasago | Mastusada | ITECH/B&K | Picotest |
| --- | --- | --- | --- | --- | --- |
|  | PFR-100 | KX-100 | P4K | 6720/9110 | P9610A |
| Maximum Output Voltage | 250 V | 160 V | 320 V (◎) | 60 V | 36 V (▲) |
| Maximum Output Current | 10 A | 10 A | 10 A | 5 A | 7 A |
| Maximum Output Power | 100 W | 100 W | 80 W (▲) | 100 W | 108 W |
| Multi-Range | 5 (◎) | 4 | 2 | 1.8 - 2.3 | 2.3 |
| Front Panel Display | LED | LED | LED | LED | LCD (◎) |
| Output ON/OFF Delay | ◎ | X | ◎ | X | X |
| CV/CC Priority | ◎ | X | X | X | X |
| CV/CC Slew Rate | ◎ | X | ◎ | X | X |
| Bleeder ON/OFF | ◎ | ◎ | X | X | X |
| OCP Delay Setting | ◎ | X | X | X | X |
| Measurement Average Setting | ◎ | X | X | X | X |
| Test Scrip (Sequence) on Front Panel | ◎ | X | X | X | X |
| Memory Function on Front Panel (3 Sets) | ◎ | ◎ | ◎ | X | X |
| Interface | Front USB | ◎ | X | X | X | X |
|  | Rear USB | ◎ | ▲ (Adaptor) | ▲ (Adaptor) | X | ○ (Factory) |
|  | LAN | ○ (Factory) | ▲ (Adaptor) | ▲ (Adaptor) | X | X |
|  | RS-232 | ◎ | ◎ | ▲ (Adaptor) | ▲ (Factory Only) | X |
|  | RS-485 | ◎ | ▲ (Adaptor) | ▲ (Adaptor) | X | X |
|  | GPIB | ○ (Factory) | ▲ (Adaptor) | ▲ (Adaptor) | X | ○ (Factory) |
|  | External Analog Control | ◎ | ▲ (Output Only) | ▲ (Output Only) | X | X |
| Protection | OVP | ○ | ○ | ○ | ○ | ○ |
|  | UVL | ○ | X | X | X | X |
|  | OCP | ○ | ○ | ○ | ○ | ○ |
|  | OTP | ○ | ○ | ○ | ○ | ○ |
|  | AC Fail | ○ | X | ○ | X | X |
| Others | Dimensions (W×H×D) mm | 3U (70 × 124 × 300) | 3U (71 × 130 × 300) | 3U (35 × 124 × 270) | 4U (▲) (88 × 175 × 282) | 2U (214.6 × 88.6 × 280) |
|  | Power Density (W/cm3) | 0.038 | 0.036 | 0.068 | 0.023 | 0.020 |
|  | Fanless | ◎ | ◎ | ◎ | X | X |
|  | Output Terminal | ◎ Front / Rear | ◎ Front / Rear | ◎ Front / Rear | ○ Front | ○ Front |
|  | Universal Input | ◎ | X (Factory) | ◎ | ○ (Switch) | ○ (Switch) |
|  | CE Mark | ◎ | X | X | X | ◎ |

◎: Excellent/ ○: Good/ ▲: Bad/  X: None

SPECIFICATION

### Output

| Model |  |  | PFR-100L | PFR-100M |
| --- | --- | --- | --- | --- |
| Rated Output Voltage |  | V | 50 | 250 |
| Rated Output Current |  | A | 10 | 2 |
| Rated Output Power |  | W | 100 | 100 |
| Power ratio |  | --- | 5 | 5 |

### Constant Voltage Mode

| Model |  |  | PFR-100L | PFR-100M |
| --- | --- | --- | --- | --- |
| Line regulation(*1) |  | mV | 8 | 30 |
| Load regulation (*2) |  | mV | 10 | 33 |
| Ripple and noise (*3) | p-p (*4) | mV | 50 | 150 |
|  | r.m.s. (*5) | mV | 4 | 15 |
| Temperature coefficient (after a 30 minute warm-up) |  | ppm/ °C | 100 | 100 |
| Remote sense compensation voltage (single wire) |  | V | 1 | 1 |
| Rise time (*6) | Rated load | ms | 50 | 100 |
|  | No load | ms | 50 | 100 |
| Fall time (*7) | Rated load | ms | 100 | 200 |
|  | No load | ms | 500 | 1000 |
| Transient response time (*8) |  | ms | 1.5 | 2 |

### Constant Current Mode

| Model |  |  | PFR-100L | PFR-100M |
| --- | --- | --- | --- | --- |
| Line regulation (*1) |  | mA | 8 | 1.2 |
| Load regulation (*9) |  | mA | 10 | 3.2 |
| Ripple and noise | r.m.s. | mA | 10 | 2 |
| Temperature coefficient (after a 30 minute warm-up) |  | ppm/ °C | 200 | 200 |

### Protection Function

| Model |  |  | PFR-100L | PFR-100M |
| --- | --- | --- | --- | --- |
| Over voltage protection (OVP) | Setting range | V | 5 - 55 | 5 - 275 |
|  | Setting accuracy | V | 0.50 | 2.5 |
| Over current protection (OCP) | Setting range | A | 1 - 11 | 0.2 - 2.2 |
|  | Setting accuracy | A | 0.20 | 0.040 |
| Under voltage limit (UVL) | Setting range | V | 0 - 52.5 | 0 - 262.5 |
| Over temperature protection (OTP) | Operation | Turn the output off. |
| Low AC input protection (AC-FAIL) | Operation | Turn the output off. |
| Shutdown (SD) | Operation | Turn the output off. |
| Over Power protection (OPP) | Operation | Turn the output off. |
|  | Value (fixed) | When output power is over 103% of rated power, the output will be turned off. |

### Analog Programming and Monitoring

| Model |  |  | PFR-100L | PFR-100M |
| --- | --- | --- | --- | --- |
| External voltage control output voltage | Accuracy | V | 0.50 | 2.50 |
| External voltage control output current | Accuracy | mA | 100 | 20 |
| External resistor control output voltage | Accuracy | V | 1.00 | 5.00 |
| External resistor control output current | Accuracy | mA | 200 | 40 |
| Output voltage monitor | Accuracy | V | 0.10 | 0.10 |
| Output current monitor | Accuracy | V | 0.10 | 0.10 |
| Shutdown control |  | Turns the output off with a LOW (0V to 0.5V) or short-circuit. |
| Output on/off control |  | Possible logic selections: Turn the output on using a LOW (0V to 0.5V) or short-circuit, turn the output off using a HIGH (4.5V to 5V) or open-circuit. Turn the output on using a HIGH (4.5V to 5V) or open-circuit, turn the output off using a LOW (0V to 0.5V) or short-circuit. |
| Alarm clear control |  | Clear alarms with a LOW (0V to 0.5V) or short-circuit. |
| CV/CC/ALM/PWR OFF/OUT ON indicator |  | Photocoupler open collector output; Maximum voltage 30V, maximum sink current 8mA. |

### Front Panel

| Model |  |  | PFR-100L | PFR-100M |
| --- | --- | --- | --- | --- |
| Output voltage setting range |  | V | 0 - 52.5 | 0 - 262.5 |
| Output voltage resolution |  | mV | 10 | 100 |
| Output current setting range |  | A | 0 - 10.5 | 0 - 2.1 |
| Output current resolution |  | mA | 10 | 1 |
| Display, 4 digits | Voltage accuracy | 0.1% of reading + | mV | 40 | 200 |
|  | Current accuracy | 0.2% of reading + | mA | 20 | 2 |
| Indications |  | GREEN LED's: CV, CC, VSR, ISR, DLY, RMT, LAN, M1, M2, M3, RUN |
|  |  | RED LED's: ALM, ERR |
| Buttons |  | Function(M1), Test(M2), Set(M3), Shift(PWR_DSPL), Lock/Local(Unlock), PROT(ALM_CLR), Output |
| Knobs |  | Voltage, Current |
| USB port |  | Type A USB connector |
| Binding Post |  | RED: Positive output, BLACK: Negative output, GREEN: Earth ground |

### Programming and Measurement (RS-232/485, USB, LAN, GPIB)

| Model |  |  | PFR-100L | PFR-100M |
| --- | --- | --- | --- | --- |
| Output voltage programming accuracy | 0.1% of setting + | mV | 40 | 200 |
| Output current programming accuracy | 0.2% of setting + | mA | 20 | 2 |
| Output voltage programming resolution |  | mV | 2 | 10 |
| Output current programming resolution |  | mA | 1 | 0.1 |
| Output voltage measurement accuracy | 0.1% of reading + | mV | 40 | 200 |
| Output current measurement accuracy | 0.2% of reading + | mA | 20 | 2 |
| Output voltage measurement resolution |  | mV | 2 | 10 |
| Output current measurement resolution |  | mA | 1 | 0.1 |

### Input Characteristics

| Model |  |  | PFR-100L | PFR-100M |
| --- | --- | --- | --- | --- |
| Input voltage range |  | Vac | 85-265 |
| Input frequency range |  | Hz | 47-63 |
| Maximum input current | 100Vac | A | 1.5 | 1.44 |
|  | 200Vac | A | 0.75 | 0.72 |
| Inrush current |  |  | Less than 20A. |
| Maximum input power |  | VA | 150 |
| Power factor | 100Vac |  | 0.98 |
|  | 200Vac |  | 0.95 |
| Efficiency | 100Vac | % | 70 | 72 |
|  | 200Vac | % | 72 | 74 |
| Hold-up time |  |  | 20ms or greater |

### Interface Capabilities

| Model | PFR-100L | PFR-100M |
| --- | --- | --- |
| USB | Type A: Host, Type B: Slave, Speed: 1.1, USB Class:CDC (communications Device Class), TMC (Test & Measurement Class) |
| RS-232/RS-485 | Complies with the EIA-RS-232/RS-485 specifications (excluding the connector) |
| LAN (Factory Optional) | MAC Address, DNS IP Address, User Password, Gateway IP Address, Instrument IP Address, Subnet Mask |
| GPIB (Factory Optional) | SCPI-1993, IEEE 488.2 compliant interface |

### Environment Conditions

| Model | PFR-100L | PFR-100M |
| --- | --- | --- |
| Operating temperature | 0˚C to 40˚C |
| Storage temperature | -20˚C to 70˚C |
| Operating humidity | 20% to 80% RH; No condensation |
| Storage humidity | 20% to 85% RH; No condensation |
| Altitude | Maximum 2000m |

| Notes: |  |  |  |
| --- | --- | --- | --- |
| *1: At 85 ~ 132Vac or 170 ~ 265Vac, constant load. |
| *2: From No-load to Full-load, constant input voltage. Measured at the sensing point in Remote Sense. |
| *3: Measure with JEITA RC-9131B (1:1) probe |  |
| *4: Measurement frequency bandwidth is 10Hz to 20MHz. |
| *5: Measurement frequency bandwidth is 5Hz to 1MHz. |
| *6: From 10% to 90% of rated output voltage, with rated resistive load. |
| *7: From 90% to 10% of rated output voltage, with rated resistive load. |
| *8: Time for output voltage to recover within 0.1% + 10mV of its rated output |
| for a load change from 50 to 100% of its rated output current. |
| *9: For load voltage change, equal to the unit voltage rating, constant input voltage. |

Should you have any questions on the PFR-100 announcement, please don’t hesitate to contact us.

Sincerely yours,

Overseas Sales Department

Good Will Instrument Co., Ltd

No. 7-1, Jhongsing Road, Tucheng Dist.,

New Taipei City 23678, Taiwan R.O.C

Email: marketing@goodwill.com.tw

# Text boxes

GW Instek

PFR-100 Fanless Multi-Range D.C. Power Supply

New Product Announcement

This document allows GW Instek's partners to quickly grasp product's main features, FAB and ordering information.

Rear

Front